## Slide 1
CS331: COMPUTER NETWORKS PROJECT
Scalable Network I/O:
From select to io_uring
An Empirical & Architectural Analysis of Linux Socket Multiplexing
Suchith
Architecture Lead & io_uring
Rohith
epoll (ET) & Sockets
Harshith
select & poll Engines
Hanook
Benchmarking

## Slide 2
Modern high-concurrency network servers quickly break down under the C10K Concurrency Barrier when using traditional paradigms. We set out to solve three core bottlenecks:
Objective: Systematically build, profile, and compare 5 distinct Linux TCP socket paradigms from scratch under extreme load (up to 5,000+ connections).
•
Thread Stack Exhaustion: Traditional blocking servers allocate ~8MB per thread. 1,000 connections instantly consume gigabytes of RAM.
•
Context Switch Thrashing: The CPU wastes over 90% of its cycles swapping registers and invalidating caches instead of serving requests.
•
O(N) Syscall Overhead: Early multiplexers force the kernel to scan every single socket descriptor per event, devastating throughput.
1. Problem Statement & Objectives

## Slide 3
To understand the paradigm shift, we engineered five standalone C TCP servers, moving from synchronous readiness polling to zero-syscall asynchronous completion rings.
1. Blocking I/O
Thread-per-client model. Spawns via pthread_create(). Incurs massive memory and scheduling overhead.
2. select & poll
Synchronous readiness. Iterates arrays in O(N) time. select hits a strict 1024 FD cap.
3. epoll (ET)
Uses kernel Red-Black Trees for O(1) ready lists. Edge-Triggered mode highly optimizes throughput.
4. io_uring
Asynchronous Completion. Uses shared memory Ring Buffers (SQ/CQ) to achieve Zero per-I/O Syscalls.
2. Architecture & Mechanism

## Slide 4
Harness & Verification Built
We built custom Python tools extending the C server codebase to ensure rigorous functional validation:
Empirical Evaluation Results
Our benchmark revealed distinct architectural advantages across different scales:
•
Automated Test Suite: Developed test_servers.py to verify exact payload echo integrity across all 5 engines.
•
Async Load Generator: Created benchmark.py utilizing Python's asyncio to generate 5,000+ persistent connections without client-side bottlenecking.
•
Result: Achieved a 100% test pass rate and resolved memory leak bugs during socket cleanup phases.
•
Small Scale Peak: poll() achieved the highest peak throughput (59k req/s at 100 conns) due to low structural overhead for small arrays.
•
The select() Crash: Confirmed select() completely drops traffic beyond 1024 connections due to the FD_SETSIZE hard limit.
•
High Scale Stability: epoll() proved to be the most stable, sustaining 28.1k req/s at the 5,000 connection mark.
3. Extension, Issues Fixed & Evaluation

## Slide 5
Comparison of Performance, Scalability (Memory footprint), and Reliability limits at a load of 5,000 persistent connections.
I/O Paradigm | Performance (Throughput) | Scalability (VmRSS Memory) | Reliability Limits
Blocking | Degraded (3,984 req/s) | Poor (26.8 MB) | High thread crash risk
select() | Good (at low scale) | Excellent (1.2 MB) | Fails at 1024 FDs
poll() | Peak High (26,569 req/s) | Excellent (1.2 MB) | O(N) CPU strain
epoll (ET) | Highly Stable (28,142 req/s) | Best (1.5 MB) | Production Standard
io_uring | High (21,543 req/s) | Excellent (2.0 MB) | Zero-syscall stability
4. Non-Functional Testing Parameters

## Slide 6
The select() FD_SETSIZE Hard Cap: Our initial `select` server crashed violently when load testing exceeded 1024 connections. We had to implement an explicit guard check if (client_fd >= FD_SETSIZE) to cleanly reject overflow connections and prevent stack corruption.
Draining Edge-Triggered Buffers: Because `epoll` was configured in Edge-Triggered (EPOLLET) mode, it only notifies state transitions once. We learned the hard way that missing a while(1) read loop until EAGAIN leaves payload bytes stuck in socket buffers forever, breaking the server.
io_uring Complexity & State Tracking: Unlike readiness models, completion queues are fully asynchronous. Managing application state between the Submission Queue (SQ) and Completion Queue (CQ) required building a robust custom struct conn_info linked via io_uring_sqe_set_data().
5. Key Technical Challenges Faced